## Slide 1
Roaming Security
Video 6.6
Core Principles for Network Security

## Slide 2: Roaming
A mobile device being used outside the range or domain of its registered home network, where it connects to another available mobile network.
Notes: Something that needs to grab the viewers attention!!

## Slide 3
5G SA Architecture
User
Equipment
(UE)
Radio
Access Network
(RAN)
Core Network (CN)
gNodeB
IP
Network
5G Core
DU
CU
NEF
NRF
PCF
UDM
AUSF
AMF
SMF
NSSF
MEC: Multi-access Edge Computing
5G
UE
MEC

## Slide 4
5G Roaming Architecture
Core Network (CN)
5G
UE
SEPP
UPF
SEPP
IPX
UPF
IP
Network
Home
Public Land Mobile Network
(HPLMN)
SEPP: Security Edge Protection Proxy
IPX: Internet Protocol Packet Exchange
GTP-U: GPRS Tunnelling Protocol – User
Visited
Public Land Mobile Network
(VPLMN)
Core Network (CN)
GTP-U
GTP-U

## Slide 5
5G Roaming Architecture
Core Network (CN)
5G
UE
SEPP
UPF
SEPP
IPX
UPF
IP
Network
Home
Public Land Mobile Network
(HPLMN)
SEPP: Security Edge Protection Proxy
IPX: Internet Protocol Packet Exchange
GTP-U: GPRS Tunnelling Protocol – User
Visited
Public Land Mobile Network
(VPLMN)
Core Network (CN)
GTP-U
GTP-U
IPX
N32 Interface
N9 Interface
N9 Interface

## Slide 6
Visited AMF (Access and Mobility Function) requests authentication parameters from home AUSF (Authentication Server Function).
  Passes through SEPPs at edge and IPX.
Home AUSF provides visited network name provided to UDM (Unified Data Management).
  Creates 5G Home Environment Authentication Vector (5G HEAV).
  Passed back to Home AUSF.
Home AUSF sends 5G HEAV to Visited AMF.
  Becomes 5G Serving Environment Authentication Vector (SEAV).
5G Roaming Authentication

## Slide 7
Visited AMF triggers authentication towards UE (User Equipment).
UE utilizes algorithms to validate communication between networks.
Response provided to visited AMF and forwarded to home AUSF.
Keys exchanged to provide secure Control Plane and User Plane traffic.
5G Roaming Authentication

## Slide 8: Core Principles
5G Roaming Security
Secure Design Protect network and limit network function exposure.
Secure Entry Filter traffic and utilize network edge security.
Secure Communication Protect Control Plane and User Plane traffic via encryption.
Secure Procedures Implement and maintain security to protect network.

## Slide 9
Key Takeaways
Standard Roaming Architecture
SEPPs, IPXs, and secure protocols.
Authentication via Both Networks
Authentication and Authorization are essential.
Core Principles
Secure design, communication, entry, and procedures.
01
02
03

## Slide 10
Section Summary
Next Video