## Slide 1
Disclosure of Subscriber Unique Identifier
Video 7.4
Vulnerability, Threat Vectors, and Mitigation

## Slide 2
SUPI and SUCI
Mobile Country Code (MCC)
Mobile Network Code (MNC)
Mobile Subscriber Identity Number (MSIN)
3 digits
2 or 3 digits
Not more than 15 digits
International Mobile Subscription Identity (IMSI)
SUPI Type
Home Network Identifier
Routing Indicator
Protection Scheme ID
Home Network Public Key ID
Scheme Output
0: IMSI
In 5G, this becomes Subscription Permanent Identifier (SUPI)
Subscription Concealed Identifier (SUCI)
MCC + MNC
1 to 4 digits to route signaling for SUCI to AUSF and UDM
Identifier for protection scheme used for SUCI
Range 0 to 255, public key provisioned by HPLMN
Output of public key protection scheme
Protection Scheme ID along with Home Network Private Key facilitates decryption of Scheme Output to de-conceal MSIN
UDM
Core
ARPF
SIDF
Notes: 3GPP TS 23.003

## Slide 3
Core Vulnerabilities and Mitigation
Unified Data Management (UDM)
  Used for Subscriber management and UE-context management.
Unified Data Repository (UDR)
  Contains subscriber credentials and policy data.
  Utilizes Hardware Security Module (HSM) – needs tight security!
Secure Communication
  X.509v3 certificates should be used for authentication.
  TLS 1.2 or TLS 1.3 should be used for data in motion.
Notes: 3GPP TS 23.003

## Slide 4
Key Takeaways
Subscriber Unique Identifier at Risk
From UE to RAN and in the Core.
Steps to Protect
X.509v3 certificates and TLS 1.2 or 1.3.
Remember the Core
UDM and UDR may require tighter controls.
01
02
03

## Slide 5
Spectrum and Network Slicing Attacks
Next Video